## Slide 1: VACUUM TOILETS
Vacuum toilets are flush toilets that use suction for the removal of faeces and urine resulting in a minimal requirement of water (0.5 to 1.5 litres). Vacuum toilets provide the same level of comfort as traditional flush toilets and they help saving costs due to the minimised amount of flush water. Due to the fact that the effluent has a high organic matter content, vacuum toilets are specifically adapted for the use in combination with separate greywater and blackwater treatment; or aerobic digestion treatment for biogas production

## Slide 2: PROBLEM FACED
A lot of fresh water wastage in simple flush toilets. And also a blocking problem of wastage in pipes. With every flush a lot of fresh water waste and also high maintance.

## Slide 3: Solution of problem
A vacuum toilet is a solution of this problem ,it has a vacuum system so with every flush a very high pressure vacuum is created and it sucks the solid waste .in this a grey water is used and very little amount of fresh water is use.
A vacuum sewer or pneumatic sewer system is a method of transporting sewage from its source to a sewage treatment plant. It maintains a partial vacuum, with an air pressure below atmospheric pressure inside the pipe network and vacuum station collection vessel.
Valves open and reseal automatically when the system is used, so differential pressure can be maintained without expending much energy pumping. A single central vacuum station can collect the wastewater of several thousand individual homes, depending on terrain and the local situation.

## Slide 4: CONTROL VALVE SYSTEM
This is the better solution for larger buildings. Virtually, it is possible to add an unlimited number of toilets and the system can be expanded later on. If there is a permanent vacuum, the risk of a leakage is very low . However, energy requirement are generally high in order to maintain the vacuum constantly.
Step 1: The user pushes the push-button, the interface valve is opened and the wastewater is evacuated. Air, which also helps to transport the waste, is also sucked into the system. At the same time, the clean water valve is opened and rinsing water is sprayed into the bowl.
Step 2: The vacuum valve is closed but the water valve remains open. A small amount of fresh water is sprayed into the bowl.
Step 3: The water valve is closed, a small volume of clean water is retained in the bowl and the toilet is ready for use again.

## Slide 5: Advantages
Large water savings
No deposits in the toilet, reduced use of detergents
Very hygienic
Flexible and convenient
No deposits in the pipes
Odour-free
Facilitates reuse of urine and faeces
Applicable in many different constructions

## Slide 6: Conclusion
This toilet are best for toilet waste without wastage of the water .it is clean and hygienic, less fesh water is wastage and we use grey water. With every flush a high vacuum is created wich help for suction of solid waste.